## Slide 1: New SIT 185 Message Format
FMCC - Florian Boularan

## Slide 2: 1. DISTRESS COSPAS-SARSAT POSITION CONFIRMED UPDATE ALERT 2. MSG NO 28478 FMCC REF NO 281003 3. DETECTED AT 01 MAY 22 001751 UTC BY MEOSAR 4. DETECTION FREQUENCY 406.0314 MHZ 5. COUNTRY OF BEACON REGISTRATION 227/FRANCE 6. USER CLASS FGB - STANDARD LOCATION - PLB SERIAL NO: 4108 IDENTIFICATION 335/4108 7. EMERGENCY CODE NIL 8. POSITIONS CONFIRMED - 47 02.4N 002 53.7W DOPPLER A - NIL DOPPLER B - NIL DOA – 47 02.4N 002 53.7W EXPECTED ACCURACY 2NMS ENCODED - 47 04.60N 002 55.06W GNSS ALTITUDE 00160 METRES UPDATE TIME WITHIN 4 HOURS OF DETECTION TIME 9. ENCODED POSITION PROVIDED BY INTERNAL 10. NEXT PASS / EXPECTED DATA TIMES CONFIRMED - NIL DOPPLER A - UNKNOWN DOPPLER B - UNKNOWN DOA - UNKNOWN ENCODED - NIL 11. HEX ID 1C6EA7A018FFBFF HOMING SIGNAL 121.5 MHZ 12. ACTIVATION TYPE NIL 13. BEACON NUMBER ON AIRCRAFT OR VESSEL NO. NIL 14. OTHER ENCODED INFORMATION ACR ELECTRONICS INC. TAC 335 BEACON MODEL - PLB-400 / PLB-425 ENCODED POSITION UNCERTAINTY : PLUS-MINUS 2 SECONDS OF LATITUDE AND LONGITUDE 15. OPERATIONAL INFORMATION REGISTRATION INFORMATION AT FMCC BEACON REGISTRATION INFO PROVIDED IN A SEPARATE MESSAGE MEOSAR ALERT LAST DETECTED AT 01 MAY 22 001751 UTC 16. REMARKS NIL END OF MESSAGE
CONFIRMED POSITION
ENCODED POSITION
MCC REFERENCE POSITION
GNSS POSITION
POSITION UPDATE ALERT
& Logical reorganization of the message fields
Current SIT 185 Message
ESTIMATED ERROR
EXPECTED ACCURACY

## Slide 3: 1. DISTRESS COSPAS-SARSAT POSITION UPDATE ALERT 2. MSG NO 28478 FMCC REF NO 281003 3. BEACON MESSAGE INFORMATION BEACON TYPE STANDART LOCATION - PLB SERIAL NO 4108 HEX ID 1C6EA7A018FFBFF COUNTRY OF BEACON REGISTRATION 227/FRA HOMING SIGNAL 121.5 MHZ GNSS POSITION PROVIDED BY INTERNAL 4. ALERT POSITION INFORMATION DETECTED AT 01 MAY 22 001751 UTC BY MEOSAR ALERT LAST DETECTED AT 01 MAY 22 001751 UTC GNSS - 47 04.60N 002 55.06W MCC REFERENCE - 47 02.4N 002 53.7W DOA - 47 02.4N 002 53.7W ESTIMATED ERROR 2 NMS 5. OTHER INFORMATION REGISTRATION INFORMATION AT FMCC BEACON REGISTRATION INFO PROVIDED IN A SEPARATE MESSAGE TAC 335 BEACON MODEL - PLB-400 / PLB-425 DETECTION FREQUENCY 406.0314 MHZ LUT ID 2272 TOULOUSE, France 6. REMARKS NIL END OF MESSAGE
BEACON INFO
4D LOCATION
MSG ID
SYSTEM INFO*
New SIT 185 Message
*data extracted directly from the C/S System and not transmitted by the beacon itself

## Slide 4
CURRENT MESSAGE
1. DISTRESS COSPAS-SARSAT POSITION CONFIRMED UPDATE ALERT 2. MSG NO 28478 FMCC REF NO 281003 3. DETECTED AT 01 MAY 22 001751 UTC BY MEOSAR 4. DETECTION FREQUENCY 406.0314 MHZ 5. COUNTRY OF BEACON REGISTRATION 227/FRANCE 6. USER CLASS FGB - STANDARD LOCATION - PLB SERIAL NO: 4108 IDENTIFICATION 335/4108 7. EMERGENCY CODE NIL 8. POSITIONS CONFIRMED - 47 02.4N 002 53.7W DOPPLER A - NIL DOPPLER B - NIL DOA – 47 02.4N 002 53.7W EXPECTED ACCURACU 2 NMS ENCODED - 47 04.60N 002 55.06W GNSS ALTITUDE 00160 METRES UPDATE TIME WITHIN 4 HOURS OF DETECTION TIME 9. ENCODED POSITION PROVIDED BY INTERNAL 10. NEXT PASS / EXPECTED DATA TIMES CONFIRMED - NIL DOPPLER A - UNKNOWN DOPPLER B - UNKNOWN DOA - UNKNOWN ENCODED - NIL 11. HEX ID 1C6EA7A018FFBFF HOMING SIGNAL 121.5 MHZ 12. ACTIVATION TYPE NIL 13. BEACON NUMBER ON AIRCRAFT OR VESSEL NO. NIL 14. OTHER ENCODED INFORMATION ACR ELECTRONICS INC. TAC 335 BEACON MODEL - PLB-400 / PLB-425 ENCODED POSITION UNCERTAINTY : PLUS-MINUS 2 SECONDS OF LATITUDE AND LONGITUDE 15. OPERATIONAL INFORMATION REGISTRATION INFORMATION AT FMCC BEACON REGISTRATION INFO PROVIDED IN A SEPARATE MESSAGE MEOSAR ALERT LAST DETECTED AT 01 MAY 22 001751 UTC 16. REMARKS NIL END OF MESSAGE
NEW MESSAGE
1. DISTRESS COSPAS-SARSAT POSITION UPDATE ALERT
2. MSG NO 28478 FMCC REF NO 281003
3. BEACON MESSAGE INFORMATION
BEACON TYPE STANDART LOCATION - PLB
SERIAL NO 4108
HEX ID 1C6EA7A018FFBFF
COUNTRY OF BEACON REGISTRATION 227/FRA
HOMING SIGNAL 121.5 MHZ
GNSS POSITION PROVIDED BY INTERNAL
4. ALERT POSITION INFORMATION
DETECTED AT 01 MAY 22 001751 UTC BY MEOSAR
GNSS - 47 04.60N 002 55.06W
ALTITUDE 00160 METRES
UPDATE TIME WITHIN 4 HOURS OF DETECTION TIME
MCC REFERENCE - 47 02.4N 002 53.7W
DOA - 47 02.4N 002 53.7W ESTIMATED ERROR 2 NMS
ALERT LAST DETECTED AT 01 MAY 22 001751 UTC
5. OTHER INFORMATION
REGISTRATION INFORMATION AT FMCC
BEACON REGISTRATION INFO PROVIDED IN A SEPARATE MESSAGE
TAC 335
BEACON MODEL - PLB-400 / PLB-425
ENCODED POSITION UNCERTAINTY :
PLUS-MINUS 2 SECONDS OF LATITUDE AND LONGITUDE
DETECTION FREQUENCY 406.0314 MHZ
6. REMARKS NIL
END OF MESSAGE
All essential data remains

## Slide 5: Suppressed / Omitted Fields
1. DISTRESS COSPAS-SARSAT POSITION CONFIRMED UPDATE ALERT 2. MSG NO 28478 FMCC REF NO 281003 3. DETECTED AT 01 MAY 22 001751 UTC BY MEOSAR 4. DETECTION FREQUENCY 406.0314 MHZ 5. COUNTRY OF BEACON REGISTRATION 227/FRANCE 6. USER CLASS FGB - STANDARD LOCATION - PLB SERIAL NO: 4108 IDENTIFICATION 335/4108 7. EMERGENCY CODE NIL 8. POSITIONS CONFIRMED - 47 02.4N 002 53.7W DOPPLER A - NIL DOPPLER B - NIL DOA – 47 02.4N 002 53.7W EXPECTED ACCURACY 2 NMS ENCODED - 47 04.60N 002 55.06W GNSS ALTITUDE 00160 METRES UPDATE TIME WITHIN 4 HOURS OF DETECTION TIME 9. ENCODED POSITION PROVIDED BY INTERNAL 10. NEXT PASS / EXPECTED DATA TIMES CONFIRMED - NIL DOPPLER A - UNKNOWN DOPPLER B - UNKNOWN DOA - UNKNOWN ENCODED - NIL 11. HEX ID 1C6EA7A018FFBFF HOMING SIGNAL 121.5 MHZ 12. ACTIVATION TYPE NIL 13. BEACON NUMBER ON AIRCRAFT OR VESSEL NO. NIL 14. OTHER ENCODED INFORMATION ACR ELECTRONICS INC. TAC 335 BEACON MODEL - PLB-400 / PLB-425 ENCODED POSITION UNCERTAINTY : PLUS-MINUS 2 SECONDS OF LATITUDE AND LONGITUDE 15. OPERATIONAL INFORMATION REGISTRATION INFORMATION AT FMCC BEACON REGISTRATION INFO PROVIDED IN A SEPARATE MESSAGE MEOSAR ALERT LAST DETECTED AT 01 MAY 22 001751 UTC 16. REMARKS NIL END OF MESSAGE
New SIT 185 Message:
Info on the « NEXT PASS/EXPECTED DATA TIME » are suppressed
Some fields where the value is « NIL »
may be omitted
To keep the message as short
and as clear as possible

## Slide 6: Fields which may be omitted
1. DISTRESS COSPAS-SARSAT POSITION UPDATE ALERT
2. MSG NO 28478 FMCC REF NO 281003
3. BEACON MESSAGE INFORMATION
BEACON TYPE STANDART LOCATION - PLB
SERIAL NO 4108
HEX ID 1C6EA7A018FFBFF
COUNTRY OF BEACON REGISTRATION 227/FRA
HOMING SIGNAL 121.5 MHZ
GNSS POSITION PROVIDED BY INTERNAL
4. ALERT POSITION INFORMATION
DETECTED AT 01 MAY 22 001751 UTC BY MEOSAR
GNSS - 47 04.60N 002 55.06W
ALTITUDE 00160 METRES
UPDATE TIME WITHIN 4 HOURS OF DETECTION TIME
MCC REFERENCE - 47 02.4N 002 53.7W
DOA - 47 02.4N 002 53.7W ESTIMATED ERROR 2 NMS
ALERT LAST DETECTED AT 01 MAY 22 001751 UTC
5. OTHER INFORMATION
REGISTRATION INFORMATION AT FMCC
BEACON REGISTRATION INFO PROVIDED IN A SEPARATE MESSAGE
TAC 335
BEACON MODEL - PLB-400 / PLB-425
ENCODED POSITION UNCERTAINTY :
PLUS-MINUS 2 SECONDS OF LATITUDE AND LONGITUDE
DETECTION FREQUENCY 406.0314 MHZ
6. REMARKS NIL
END OF MESSAGE
A shorter and more concise new SIT 185 message
LISTING
3.
TYPE OF BEACON
IDENTIFICATION
COUNTRY OF BEACON REGISTRATION
BEACON NUMBER
HOMING SIGNAL
ACTIVATION TYPE
SOURCE OF GNSS POSITION DATA
EMERGENCY CODE
4.
GNSS POSITION, TIME OF UPDATE AND ALTITUDE
MCC REFERENCE POSITION
DOA POSITION AND ALTITUDE
POSITION & PROBABILITY
POSITION & PROBABILITY
5.
OTHER ENCODED INFORMATION
« NIL »: Case of a badly coded or badly decoded beacon
« NIL »: Case of a beacon badly or not localized (I.E.masking, satellites configuration… etc)

## Slide 7: Optional Information
On line 5 “OTHER INFORMATION”
LUT ID,
Number of MEOSAR satellites,
Number of packets used to generate the alert.
1. DISTRESS COSPAS-SARSAT POSITION UPDATE ALERT
2. MSG NO 28478 FMCC REF NO 281003
3. BEACON MESSAGE INFORMATION
BEACON TYPE STANDART LOCATION - PLB
SERIAL NO 4108
HEX ID 1C6EA7A018FFBFF
COUNTRY OF BEACON REGISTRATION 227/FRA
HOMING SIGNAL 121.5 MHZ
GNSS POSITION PROVIDED BY INTERNAL
4. ALERT POSITION INFORMATION
DETECTED AT 01 MAY 22 001751 UTC BY MEOSAR
GNSS - 47 04.60N 002 55.06W
ALTITUDE 00160 METRES
UPDATE TIME WITHIN 4 HOURS OF DETECTION TIME
MCC REFERENCE - 47 02.4N 002 53.7W
DOA - 47 02.4N 002 53.7W EXPECTED ERROR 2 NMS
ALERT LAST DETECTED AT 01 MAY 22 001751 UTC
5. OTHER INFORMATION
REGISTRATION INFORMATION AT FMCC
BEACON REGISTRATION INFO PROVIDED IN A SEPARATE MESSAGE
TAC 335
BEACON MODEL - PLB-400 / PLB-425
ENCODED POSITION UNCERTAINTY :
PLUS-MINUS 2 SECONDS OF LATITUDE AND LONGITUDE
DETECTION FREQUENCY 406.0314 MHZ
6. REMARKS NIL
END OF MESSAGE